## Slide 1: Unit-5 Domain Specific Applications of IoT
bhushan.joshi@darshan.ac.in
+91 8485979997
Computer Engineering Department
Prof. Bhushan D. Joshi
Internet of Things (IoT)
DU #2101CS631

## Slide 2: Domain Specific applications of IoT
Home automation, Industry applications, Surveillance applications & Other IoT applications
IoT Application Architecture
Introduction to Python And Different IoT tools
Developing IoT application through IoT tools
Developing sensor-based application through embedded system platform
IoT and Cloud computing

## Slide 3: IoT Applications
Section - 1

## Slide 4: Applications with IoT
Using IoT we can build many applications but here, few IoT Applications will be discussed.
We will cover following topics of the IoT applications.
  Overview – General Practice
  Importance – Why we need?
  Requirements – Materials and Facility
  Architecture – Functional Block Diagram
  How it works – General Working of IoT Applications
Before we explore them one by one, let’s understand the common architecture of the IoT applications.
Notes: 4

## Slide 5
Internet
Within Organization for
Local Analysis, Processing and Controlling
Common Architecture for IoT Application
Cloud Services
Central and Remote
Storage/Analysis
Internet Gateway
Where, Link: Wire, LAN, Wi-Fi, or Bluetooth Connectivity
Controller Node
Link
Fog / Local Computer
Link
Sensor Nodes
All Kind of Sensors,
GPS, etc.
Actuator Nodes
Relays, Alarms, Motors, Actuators, Light Indicators, etc.
Local Monitoring
Link
In House Monitoring or Care Taker Team Members
Remote Monitoring
Data Analytics
Research / Decision Making
Internet
Remote Monitoring or Care Taker or Emergency Help Team Members.
This “Local Analysis, Processing and Controlling” section may not be there in many IoT solutions
Notes: 5

## Slide 6
Internet
Within Organization for
Local Analysis, Processing and Controlling
Common Architecture for IoT Application
Cloud Services
Central and Remote
Storage/Analysis
Internet Gateway
Where, Link: Wire, LAN, Wi-Fi, or Bluetooth Connectivity
Controller Node
Link
Fog / Local Computer
Link
Actuator Nodes
Relays, Alarms, Motors, Actuators, Light Indicators, etc.
Sensor Nodes
All Kind of Sensors, GPS, etc.
Local Monitoring
Link
In House Monitoring or Care Taker Team Members
Remote Monitoring
Data Analytics
Research / Decision Making
Internet
Remote Monitoring or Care Taker or Emergency Help Team Members.
This Local Analysis, Processing and Controlling section may not be there in many IoT solution
Notes: 6

## Slide 7: How it works?
Gateway
Actuator Node
Sensor Node
Sensor Node
Sensor Node
Actuator Node
All the sensor and actuator nodes should be placed at appropriate place.
The sensor and actuator nodes should have proper connectivity with controller nodes or direct to the cloud server.
The sensor nodes sends the sensed data to the controller nodes or directly to the cloud server.
The controller node:
  Collects the data from all the sensors.
  Apply some business logic on it as per the requirements
  Send it to the Fog or local computer, or directly to the cloud server.
Sensor / Actuators
Notes: 7

## Slide 8: How it works?
All the controller nodes should have connected with the Fog or local computer network, or directly to the cloud server via Internet.
Fog or local computer
  Receives all the data from all the controller nodes,
  Execute some business logic and
  Do analysis on the collected data, and
  Send the filtered limited data to the cloud computer as well as
  Send the alert messages to the local team.
The Fog computer should have Internet connectivity for the cloud connectivity.
Fog Computing
Notes: 8

## Slide 9
How it works?
All the in House Monitoring team members can access status of all the sensors from the Fog/Local computer.
The cloud
  Stores all the data received from the Fog/Local computer or directly from the sensors,
  Execute some business logic and
  Do analysis on the stored data.
All those who have rights to access the cloud data can get desire information from it, like
  Remote monitoring team members,
  Data analytics
Cloud Computing
Notes: 9

## Slide 10
How it works?
The care taker and data analytics teams may execute corrective action based on the analyzed data.
They may
  Send command to the local computer or to the actuators directly and
  Broadcast alert messages to the concern persons.
All the actuator nodes receives command from the cloud directly or from the controller or local computer.
The “Local Analysis, Processing and Controlling” section may not be there in many IoT solutions.
Data Analytics & Action
Notes: 10

## Slide 11: Health Care Application
Section - 2

## Slide 12
Healthcare Application with IoT
The healthcare sector consists of medical and related goods and services.
Healthcare sector provides medical services for maintaining or improving health via
  Prevention
  Diagnosis
  Treatment
  Recovery or cure of disease, illness, injury, and other physical and mental harms in people.
Healthcare sector is much diversified and is full of opportunities in every segment.
Overview
Notes: 12

## Slide 13
Healthcare Application with IoT
Healthcare is delivered by health professionals.
  Medicine
  Dentistry
  Pharmacy
  Nursing
  Psychology
  And other health professions are all part of health care.
Healthcare has become one of India’s largest sector in terms of revenue and employment.
Overview
Notes: 13

## Slide 14
Healthcare Application with IoT
Before Internet of Things, patients’ interactions with doctors were limited to visits.
There was no way doctors or hospitals could monitor patients’ health continuously.
IoT enabled devices have made remote monitoring in the healthcare sector possible.
IoT helps
  To keep patients safe and healthy,
  Empowering physicians to deliver superlative care.
Importance
Notes: 14

## Slide 15
Healthcare Application with IoT
Remote monitoring of patient’s health helps in
  Reducing the length of hospital stay and
  Prevents re-admissions.
IoT has applications in healthcare that benefit to
  Patients
  Families
  Physicians
  Hospitals and
  Insurance
Importance
Notes: 15

## Slide 16
Healthcare Application with IoT
Sensors
  Heartbeat Sensor
  Oxygen Level Sensor
  Glucose Level Sensor
Controller
  ESP8266 Node MCU or
  Arduino Uno with Wi-Fi or Network Shield
For Fog Computing
  Raspberry Pi or
  PC
LAN and WAN Connectivity
  Router and Switches
  Wireless Access Point
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet
Requirements for IoT Setup
Notes: 16

## Slide 17
Healthcare Application with IoT
Heartbeat Sensor Node
Oxygen Sensor Node
Glucose Sensor Node
Patients Family
Cloud Services
Central and Remote
Storage/Analysis
Fog Computer
Within Organization for Local Analysis and Processing
Local Care Taker Monitoring
Nursing Staff and Doctors
Remote Care Taker Monitoring
Nursing Staff and Doctors
Data Analytics
Research / Decision Making
Controller Node
Patient Wise Node
Wi-Fi
Wi-Fi
Wi-Fi
Wi-Fi LAN
Internet Gateway
Internet
Internet
Internet
Wi-Fi / LAN
Architecture
Notes: 17

## Slide 18
Healthcare Application with IoT
All the sensor nodes should be placed on patient body, either direct or using wearables.
The sensor nodes should have Wi-Fi connectivity with a controller node of the patient.
The sensor nodes sends the sensed data to the controller node.
The controller node collects
  The data from all the sensors,
  Apply some business logic on it as per the requirements and
  Send it to Fog computer.
All the controller nodes of all the patients should have connected with the Fog computer network.
How it works?
Notes: 18

## Slide 19
Healthcare Application with IoT
Fog computer
  Receives all the data from all the controller nodes
  Execute some business logic and
  Do analysis on the collected data, and
  Send the filtered limited data to the cloud computer as well as
  Send the alert messages to the care taker team (nursing staff and doctors).
The Fog computer should have Internet connectivity for the cloud communication.
All the local care taker team members can be accessed health status of all the patients from the Fog computer.
How it works?
Notes: 19

## Slide 20
Healthcare Application with IoT
The cloud
  Stores all the data received from the Fog
  Execute some business logic
  Do analysis on the stored data
All those who have rights to access the cloud data can get health records of the patients, like
  Remote care taker team members
  Data analytics team
  Patient family members
The care taker and data analytics teams may execute corrective action based on the data and alert messages.
How it works?
Notes: 20

## Slide 21
Healthcare Application with IoT
IoT has changed people’s lives by enabling constant tracking of health conditions.
Wearables connected devices like blood pressure and heart rate monitoring cuffs, glucometer etc. give patients attention.
On any changes in the routine activities of a person, alert message sends to family members and health service providers.
IoT enables healthcare professionals to be more watchful.
Data collected from IoT devices can help physicians identify the best treatment process.
IoT devices tagged with sensors are used for tracking real time location of medical equipment like wheelchairs, nebulizers, oxygen pumps and other monitoring equipment.
IoT-enabled hygiene monitoring devices help in preventing patients from getting infected.
It also help in asset management like pharmacy inventory control, and environmental monitoring, for instance, checking refrigerator temperature.
Summary
Notes: 21

## Slide 22: Retail Applications
Section - 3

## Slide 23
IoT Application in Retail
Retail is the process of selling consumer goods or services to end-users for earning a profit.
The retail sectors can be divided into
  Food
  Clothing & Textiles
  Consumer Durables
  Footwear
  Jewelry
  FMCG
Overview
Notes: 23

## Slide 24
IoT Application in Retail
In the retail industry customer plays key roll
The retail industry is rapidly transforming with IoT solutions.
IoT is taking the center stage in the sector.
Inventory management has been an expensive and tedious process.
IoT system automatically monitors inventory.
Send alert messages to managers if a certain item is running low or going to expire soon.
IoT devices are also helpful for avoiding
  Oversupply
  Shortage of goods and
  Thefts in stores
Importance
Notes: 24

## Slide 25
IoT Application in Retail
Customers are notified about discounts and offers in real-time.
It give data about customer behavior and routes.
IoT helps to increase
  Customer loyalty
  Boost sales
  Offer a personalized experience
  Helps to maintain Stock
Importance
Notes: 25

## Slide 26
IoT Application in Retail
Controller
  ESP32 MCU or
  Arduino Uno with Wi-Fi or Network Shield
LAN and WAN Connectivity
  Router and Switches
  Wireless Access Point
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet
  Alarm
  Water Sprinkler
  Beacons
  RFID Tag and RFID Reader
Sensors | Actuators and Tags
  Touch Sensors
  Gas Sensors
  Fire Sensors
  IR Sensors
Requirements for IoT Setup
Notes: 26

## Slide 27
IoT Application in Retail
Local Server
Within Organization for Local Analysis and Processing
Wi-Fi LAN
Cloud Services
Central
Storage/Analysis
Internet Gateway
Monitoring System
Store Manager and Other Staff
Internet
Data Analytics
Research / Decision Making
Internet
Customers
Internet
Wi-Fi / LAN
RFID Readers
On Smart Shelves
Controller Nodes
Wi-Fi
Wi-Fi
Wi-Fi
Touch Sensor Nodes
Gas & Fire Sensor Nodes
Light & Temp. Sensor Nodes
Camera & IR
Sensor Nodes
For Feedback
For
Safety
For
Ambiance
For In-Store,
Entry-Exit & Parking
Alarm & Water Sprinkler Node
Wi-Fi / LAN
For Safety
Beacons
For In-store Navigation &
Real Time Offers
Bluetooth
Beacon Data
RFID Tags
On Each Item
RIFD Tag Data
For Inventory Management
Architecture
Notes: 27

## Slide 28
IoT Application in Retail
All the sensor nodes and Beacons should be placed at various places in the store, washroom and parking area.
The sensor nodes should have Wi-Fi connectivity with controller nodes.
The sensor nodes sends the sensed data to the controller nodes.
The controller nodes
  Collects the data from all the sensors,
  Apply some business logic on it as per the requirements
How it works?
Notes: 28

## Slide 29
IoT Application in Retail
RFID readers should be placed at items display shelves to detect item presence in the shelves for the stock management.
All the controller nodes and RFID readers should have connected with the Local Area Network.
RFID tags should be attached with each and every item which are likely to be monitored.
Using the RFID tags one can monitor location and stock of the item.
RFID tags is also useful for auto billing and queue less exit.
How it works?
Notes: 29

## Slide 30
IoT Application in Retail
Touch sensors are used for customers’ feedback about ambiance and cleanness at various places like washroom, trial room etc.
Light and Temperature sensors are used for ambiance monitoring which leads to energy saving and customer comfort.
Camera and IR sensors are placed for monitoring people density at various places, person in-out ratio for store and the parking area.
Gas sensors are used for monitoring various gases levels in the store.
Fire sensor are used for detecting fire in the store and send the alert signal to the Alarm & Water Sprinkler
How it works?
Notes: 30

## Slide 31
IoT Application in Retail
An alarm system and the water sprinkling system are used for fire safety, should have connected with a controller node
Local Server
  Receives all the data from all the controller nodes,
  Execute some business logic and
  Do analysis on the collected data, and
  Send the essential data to the cloud computer.
The server computer should have Internet connectivity for the cloud communication.
The cloud
  Stores all the data received from the local server,
  Execute some business logic and
  Do analysis on the stored data
How it works?
Notes: 31

## Slide 32
IoT Application in Retail
All those who have rights to access the cloud data can get desire information and alerts, like
  Store manager
  Staff members
  Data analytics team
  customers
The store manager and data analytics teams may execute corrective action based on the data.
How it works?
Notes: 32

## Slide 33
IoT Application in Retail
Beacons, a Bluetooth Low Energy (BLE) device
  Automatically connect with customers’ smartphones when they entered in the coverage area.
  Send push notifications directly to the customers.
Beacons can be installed at various places
  For customer in-store navigation,
  To know foot fall in particular area of the store, and
  Collecting data about customer behavior and routes.
Customers are notified about discounts and offers in real-time using the beacons system.
How it works?
Notes: 33

## Slide 34
IoT Application in Retail
IoT will dramatically transform and innovate the retail industry in the coming years.
The integration of IoT solutions will enable retail companies,
  To create successful marketing campaigns based on customer behavior,
  Deliver high-quality services,
  Improve inventory management, and
  Reduce operational costs.
Summary
Notes: 34

## Slide 35: Driver Assistance
Section - 4

## Slide 36
Driver Assistance Application with IoT
Vehicle manufacturing companies are trying to make vehicles more comfortable and safe for their passengers.
They are experimenting to design a system that could monitor and alert the user suffering from highway hypnosis or white line fever.
As well as they need an IoT based system to prevent accidents caused by drowsy driver.
Overview
Notes: 36

## Slide 37
Driver Assistance Application with IoT
Driver’s drowsiness is one of the major factor is reported in road accidents.
Drowsiness is a kind of sleeping sensation which can lead for closing eyes.
Drowsiness make one physically inactive and insensitive to surroundings.
So we need to monitor driver’s consciousness along with his acceleration pattern and steering angle.
If any deviation is detected, a system should be there to alert the driver.
A process of detecting the deviation and drowsiness of the driver should be developed
Importance
Notes: 37

## Slide 38
Driver Assistance Application with IoT
Using Image Processing and Machine Learning (ML) technology a system can be developed.
The system detect whether the driver has deviated or not, by monitoring the driver’s
  Facial movements
  Eye Aspects Ration (EAR) for drowsiness
  Acceleration pattern
  Change in the steering angle
Importance
Notes: 38

## Slide 39
Driver Assistance Application with IoT
Sensors
  Ultrasonic Sensor
Cameras
On Board Diagnostic (OBD) Access
Controlling
  Raspberry Pi
WAN Connectivity
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet
Requirements for IoT Setup
Notes: 39

## Slide 40
Driver Assistance Application with IoT
Cloud Services
Central and Remote
Storage/Analysis
Internet Gateway
Data Analytics
Research / Decision Making
Internet
Vehicle Owner
Internet
Alert System
Driver
Wi-Fi / Bluetooth
Vehicle Computer
Within Vehicle for Local Analysis and Processing
USB
Internet
Wired / Bluetooth
Ultrasonic Sensor Nodes
Distance
Surrounding Vehicle
Bluetooth
Steering Angle
Speed
Variation
OBD
On Board Diagnostics Unit
Deviation Detection System
Lane Detection
EAR Value
Camera
Camera Units
Drowsiness Detection System
Facial Area
Architecture
Notes: 40

## Slide 41
Driver Assistance Application with IoT
Camera units should be placed on board for capture the face of driver and road view.
The camera units should have USB connectivity with vehicle computer.
The camera units sends the sensed data to the vehicle computer.
The ultrasonic sensor nodes should be placed at various place on outside the vehicle for detecting surrounding distance.
All the sensor nodes should have Wired / Bluetooth connectivity with the Vehicle Computer.
How it works?
Notes: 41

## Slide 42
Driver Assistance Application with IoT
The OBD unit of the vehicle should have Bluetooth connectivity with the vehicle computer
The vehicle computer
  Collects the data from the camera units, OBD unit and the sensor nodes, and
  Apply some business logic,
  Do analysis on the collected data on it as per the requirements and
  Send the filtered limited data to the cloud computer as well as
  Send the alert messages to the driver.
The vehicle computer should have Internet connectivity for the cloud communication.
How it works?
Notes: 42

## Slide 43
Driver Assistance Application with IoT
The driver side camera capture the drive facial and eye movement.
The camera send the captured images to vehicle computer for EAR value and other calculation.
EAR (Eye Aspect Ratio) is measured using following equation.
EAR
  Where
    is distance between points P2 and P6
    is distance between points P3 and P5
    is distance between points P1 and P4
Using image processing the system finds the eye positions and calculate the above mentioned distance of the six points.
When the driver closes his eye, the EAR value eventually drops to zero and the system detects drowsiness of the driver.
How it works?
Notes: 43

## Slide 44
Driver Assistance Application with IoT
The road side camera capture the front view images.
The capture images sends to the vehicle computer for
  Detecting lane
  Objects
  Sign boards
Deviation is monitored using OBD (On-Board Diagnostics) device.
How it works?
Notes: 44

## Slide 45
Driver Assistance Application with IoT
OBD can record the pattern of acceleration and steering angles during the drowsiness of the driver.
Compare the recorded values with the threshold value and the historical data for the actual deviation.
All the calculated data is sent to the data analytics and obtained result, is used to alert the driver.
The cloud data also useful for the vehicle owner.
How it works?
Notes: 45

## Slide 46
Collision Impact Detection Using IoT
Modern vehicles are equipped with the collision detection mechanism.
It blow up airbags when an accident occurs and save lives in major cases.
But if the collision is massive then the airbags may not sufficient.
In these cases emergency help needed to save the lives.
So we need a system that measure the severity impact of the collision and send alert message.
Overview
Notes: 46

## Slide 47
Collision Impact Detection Using IoT
The messages contents
  Location of the accident
  Severity impact,
  Fire status,
  Speed of the vehicle,
  Number of passengers,
  Time of the incident, etc.
Broadcast the messages to all the authorities like
  Ambulance service,
  Hospitals,
  Highway patrolling team,
  Fire brigade,
  Police,
  Family member of the vehicle owner, etc.
Overview
Notes: 47

## Slide 48
Collision Impact Detection Using IoT
If a single accident occur in along highway then it can be managed without the data of severity of the collision.
When multiple accident occurs on the highway then the severity data is very important to save lives of the very serious victims.
Based on the data and severity impact, all the emergency help will be reached timely at the point.
Thus, we need an IoT based system that sense the necessary parameters of the collision.
Importance
Notes: 48

## Slide 49
Collision Impact Detection Using IoT
Sensors
  FSR Sensor
  Fire Sensor
  GPS Sensor
Cameras
OBD Access
Controlling
  Raspberry Pi
WAN Connectivity
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet
Requirements for IoT Setup
Notes: 49

## Slide 50
Collision Impact Detection Using IoT
Architecture
Cloud Services
Central and Remote
Storage/Analysis
Internet Gateway
Data Analytics
Research / Decision Making
Internet
Vehicle Owner
Family
Internet
Vehicle Computer
Within Vehicle for Local Analysis and Processing
Wired / Bluetooth
FSR
Sensor Nodes
Severity Impact
Bluetooth
Speed
OBD
On Board Diagnostics Unit
For Speed
USB
Camera
Camera Units
For Passenger Counting
Passenger Count
Emergency Help
Service Provider
Internet
Ambulance
Hospitals
Highway Patrolling
Fire Brigade
Police
GPS
Node
For Location
Wired / Bluetooth
Fire
Sensor
Node
For Detecting Fire
Wired / Bluetooth
Notes: 50

## Slide 51
Collision Impact Detection Using IoT
Force sensitive resistor (FSR) sensors are useful to measure pressure applied on the vehicle during the collision.
The FSR sensor are mounted on the vehicle at the places where impact probability is higher than the other part of vehicle during an accident.
Based on the FSR data we can estimate the severity of the collision.
Fire sensor and GPS should be placed at appropriate place of the vehicle.
All the sensor nodes should have Wired / Bluetooth connectivity with the vehicle computer.
Camera units should be placed on board for capturing all the passengers.
How it works?
Notes: 51

## Slide 52
Collision Impact Detection Using IoT
The camera units should have USB connectivity with vehicle computer.
The camera units sends the captured images to the vehicle computer.
The OBD unit of the vehicle should have Bluetooth connectivity with the vehicle computer
The vehicle computer
  Collects the data from the camera units, OBD unit and the sensor nodes.
  Apply some business logic,
  Do analysis on the collected data on it as per the requirements.
  Send the analyzed data to the cloud computer.
  Should have Internet connectivity
How it works?
Notes: 52

## Slide 53
Collision Impact Detection Using IoT
Using OBD (On-Board Diagnostics) device the system records speeds of the vehicle.
The fire sensor and GPS also sends the sensed data to the vehicle computer.
Based on the analyzed data and severity of the collision the cloud system sent alert messages to all the emergency help service provider and family member of the vehicle owner.
The cloud data is used for data analytics and to provide the priority based emergency services.
The system is automatic activated when the collision is detected.
How it works?
Notes: 53

## Slide 54: Water Quality Monitor
Section - 5

## Slide 55
Water Quality Monitoring - IoT Based Application
At present water quality is monitored very expensive and inefficient by manual or nodal network methods
Manual Method
  Water samples are taken manually from the different points of a water area.
  The samples sent to laboratories
  Various tests are conducted to find the values of
    PH, Conductivity and Temperature
    TDS, Dissolved Oxygen
    Turbidity
    Chloride Content
  The reports of the test sends to the concern authorities with in a week.
Importance
Notes: 55

## Slide 56
Water Quality Monitoring - IoT Based Application
Water is essential for life and the polluted water is a one of the major challenge in the world.
So water quality monitoring is necessary for us.
Water Quality Monitoring (WQM) helps in preventing and controlling water pollutions.
Water quality should be checked regularly to avoid serious health issues.
IoT can help to develop a perfect WQM system.
Overview
Notes: 56

## Slide 57
Water Quality Monitoring - IoT Based Application
Manual Method
The methods have some limitations like
  Chance of human error in the sampling
  Sampling cost is very high because of to cover very large area of waterbody
  Sampling and Testing both are time consuming
  Not real-time monitoring which leads to may serious issues.
Importance
Notes: 57

## Slide 58
Water Quality Monitoring - IoT Based Application
Nodal Network Method (Electronics Sensor Monitoring)
  Water quality is measured by electronic sensors installed in the different points of a water area.
  All the sensors are wirelessly connected with the Internet.
  The water quality data sends to the cloud server at regular interval.
  This method is giving real-time data contras to the manual method.
  System architecture of the monitoring system is divided into following four areas
    Sensing
    Data Collection
    Processing
    Communication
Importance
Notes: 58

## Slide 59
Water Quality Monitoring - IoT Based Application
Nodal Network Method (Electronics Sensor Monitoring)
The methods have following limitations
  Very expansive
  Maintenance of the sensors along with power source are challenging
  Natural disaster and aquatic animal movement in the waterbody may damage the sensors
  The sensors are not moveable
Importance
Notes: 59

## Slide 60
Water Quality Monitoring - IoT Based Application
A low cost solution is possible for WQM using latest technology, Data Analytics, USVs, Machine Learning, AI and IoT.
No need to install sensors permanently into the waterbody in the solution
An autonomous boat (USV), mounted with all the necessary sensors can
  Collect the water quality data and
  Send the data to the cloud for data analytics
All the necessary parameters of water can be tracked and measured.
Detailed report of the containment status of the entire waterbody can be generated.
Importance
Notes: 60

## Slide 61
Water Quality Monitoring - IoT Based Application
Controller
  ESP32 MCU or
  Arduino Uno with Wi-Fi or Network Shield
WAN Connectivity
  GPRS or GSM Module
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet
Water Sensors Kit
  PH Sensor
  GPS Sensor
  Turbidity Sensor
  TDS and Dissolved Oxygen Sensor
  Temperature Sensor
  Conductivity Sensor
Unmanned Surface Vehicle (USV)
Requirements for IoT Setup
Notes: 61

## Slide 62
Water Quality Monitoring - IoT Based Application
Cloud Services
Central and Remote
Storage/Analysis
Internet
Data Analytics
Research / Decision Making
Internet
Pollution Control Board
Internet
Report Generation
USV Controller Node
Unmanned Surface Vehicle
Wired
Water Quality Sensors Kit
GPS Sensor
Turbidity Sensor
TDS and DO Sensor
PH
Sensor
Temperature Sensor
Conductivity Sensor
Sensors Kit Controller
Node
GPRS / GSM Module
Wired
USV
Control Panel
Internet
Base Station,
USV Operator
Architecture
Notes: 62

## Slide 63
Water Quality Monitoring - IoT Based Application
A bundle of all the sensors or a water quality sensor kit should be mounted on an autonomous or unmanned surface vehicle (USV).
The USV can be operated by an embedded controller node.
The USV should have GSM or GPRS internet connectivity with the cloud server.
The sensor kit sense the following values
  PH Value of Water - PH Sensor
  Temperature of Water - Temperature Sensor
  Conductivity of Water - Conductivity Sensor
  Clarity of Water - Turbidity Sensor
  Dissolved Solid and Oxygen in Water– TDS and DO Sensor
  Location of the reading - GPS Sensor
How it works?
Notes: 63

## Slide 64
Water Quality Monitoring - IoT Based Application
The kit controller node sends all the sensed data to the cloud server via GPRS/GSM module
The GPRS/GSM module is used to provide the Internet connectivity with the cloud server.
The cloud
  stores all the data received from the USVs,
  Execute some business logic and
  Do analysis on the stored data.
All those who have rights to access the cloud data can get water quality records of the waterbody.
Like,
  Members of Pollution Control Board
  Data analytics team
  USV operator
How it works?
Notes: 64

## Slide 65
Water Quality Monitoring - IoT Based Application
Authorities of the board and data analytics teams may execute corrective action based on the data.
An USV control panel is installed in the base station of the WQM system.
The control panel should have internet connectivity for controlling the USV.
Using the control panel, an operator can set paths and control the USV.
How it works?
Notes: 65

## Slide 66: IoT with Python
Section - 6

## Slide 67: Introduction To Python : Python in IoT
Python’s popularity in IoT is attributed to its ease of use, an abundance of libraries and frameworks, and its versatility.
Python offers a rich set of tools and libraries that simplify IoT development.
Some of the best solutions for IoT in the Python programming language are as follows:
Python on Raspberry Pi
Python on PyBoard
ESP8266, ESP32 with Micropython

## Slide 68: IoT Tools
Section - 7

## Slide 69: IoT Tools
The variety of tools and platforms can be overwhelming when you’re just getting into IoT.
There are many Tools available for the development of the IoT System from prototyping to production, simple to sophisticated, open-source to commercial.
We can Classify tools as per the level of complexity like:
IoT Tools for Hobbyists and Small Projects
IoT Tools for Middle-Ranged Business Automation
Advanced IoT Tools for Enterprise and Smart Factories

## Slide 70: IoT Tools for Small Projects

## Slide 71: Hardware Platforms
Raspberry Pi is a must-have for makers and coders. This tiny yet powerful computer can connect to sensors, actuators, and other hardware. Program it with Python, Scratch, or JavaScript for limitless possibilities.
Arduino is a go-to choice for prototyping with sensors and actuators. Its simple IDE and Wiring language make it perfect for beginners and pros alike. You can connect your Arduino to the cloud with ease.
ESP8266 and ESP32 are super affordable WiFi-enabled microcontrollers.
  Program them in C/C++, MicroPython, or Arduino to build wireless projects quickly.
Adafruit Feathers are ready-to-use microcontroller boards with built-in WiFi and Bluetooth.
  Simply plug in the sensors, run the code, and you’re ready to go. Their user-friendly design gets you prototyping in no time.

## Slide 72: IoT Development Frameworks
Arduino IDE is the most popular IoT development framework, it is an open-source platform that makes creating hardware projects easy.
  The intuitive interface and simple coding language C/C++ help quickly prototype your ideas.
PlatformIO is an open-source ecosystem for IoT development, supporting a vast range of development boards and microcontrollers. It also has a robust library manager, advanced debugging tools, and continuous integration.
Thonny is a beginner-friendly IDE for Python programming with a simple interface designed for learning.
  Thonny is perfect for IoT projects using microcontrollers like the mentioned Raspberry Pi with the support of Python.
ESPHome is an open-source framework for home automation that lets you control your ESP8266/ESP32-based devices from any phone or tablet. ESPHome has a simple setup and integrates with popular smart home software.

## Slide 73: Cloud Services
Adafruit IO is an easy-to-use cloud platform to store and retrieve data from sensors, actuators, and more.
Home Assistant is an open-source home automation platform that prioritizes local control and privacy. It is powered by an active developer community producing integrations for hundreds of devices. The platform enables you to automate your lights, sensors, appliances, and much more. Home Assistant can run on your hardware or in the cloud.

## Slide 74: IoT Tools for Middle- Ranged Business

## Slide 75: Hardware Platforms
Industrial PCs offer the stability, reliability, and longevity required for IoT edge devices.With features like extended temperature range, vibration resistance, and fast processors, industrial PCs can serve as the backbone of your IoT infrastructure.
Intel’s NUC (The Next Unit of Computing) mini PCs are perfect for IoT applications that require a small footprint but plenty of processing power. The wide range of models offers different connectivity options, CPU choices, and expandability to suit various IoT needs.
Being an open-source electronics platform powered by an embedded Linux board, the tiny BeagleBone Black is packed with useful features. It offers programmable GPIOs, a USB host, an Ethernet port, and more, making it ideal for building IoT prototypes and proof of concepts.
NVIDIA Jetson modules bring the power of AI and GPU acceleration to edge devices with features like HDMI output, USB 3.0, Gigabit Ethernet, and more

## Slide 76: IoT Development Frameworks
Microsoft Azure IoT Suite is a comprehensive set of cloud services and APIs that helps you connect, monitor, and control billions of IoT assets.
  You can collect data from IoT devices at any scale, analyze the data using Azure Machine Learning, and take action on the insights using business logic.
AWS IoT Core is used to connect IoT devices to the AWS Cloud.
  It provides a managed cloud service that lets you easily supply and register millions of IoT devices and interact with them seamlessly and securely.
Google Cloud IoT Core is a fully managed service that will help you connect, manage, and ingest data from globally dispersed devices.
  It provides a scalable, efficient, and economical IoT data pipeline to Google Cloud.
IBM Watson IoT Platform helps businesses collect and organize data from billions of connected devices.
  It offers an open and scalable platform for quickly developing IoT applications and insights.

## Slide 77: Edge Computing
AWS Greengrass is perfect for running local computing, messaging, data caching, and ML inference at the edge.
  Deploy your cloud logic to connected devices so they can act locally on the data they generate while still using the AWS Cloud for management, analytics, and durable storage.
Run AI and custom business logic on edge devices with the same Azure services you use in the cloud. Azure IoT Edge extends Azure IoT to the edge of the network, enabling IoT solutions that deliver low latency to operate autonomously and access data where it’s created.
Google Cloud IoT Edge is a tool to deploy and run containerized services directly on edge devices to process data and act on it immediately. It brings AI and advanced analytics to the edge with on-device machine learning.
The future is smart, so get out there and start connecting!

## Slide 78: IoT Tools for Enterprise and Smart Factories

## Slide 79: Industrial IoT (IIoT) Hardware
Get real-time data to power automation and predictive maintenance with industrial sensors designed to withstand harsh industrial environments.
Industrial Sensors will monitor critical parameters like temperature, pressure, vibration, and flow rate.
Programmable Logic Controllers (PLCs) act as the brains of your automation system, controlling machinery and processes.
The latest PLCs offer increased processing power, connectivity options, and advanced features to support IIoT applications.
Industrial-grade PCs serve as data collection and communications hubs, connecting machines to the industrial Internet.
Human-machine interface (HMI) panels provide operators with visual feedback and control of automation systems.
Modern HMIs feature intuitive touchscreens, advanced graphics, and IoT connectivity for remote monitoring.

## Slide 80: IIoT Platforms & Solutions
Siemens MindSphere (now Insights Hub) is an advanced IIoT system that collects data from connected products and assets.
It then applies artificial intelligence and analytics to gain insights, optimizing processes and operations.
Bosch IoT Suite is a cloud-based platform connecting products and machines to the Internet of Things.
GE Predix is an industrial-grade operating system for the Industrial Internet that allows data from machines to be analyzed and used for optimization.
Predix collects data from assets and applies analytics and AI to generate insights that drive improvements in operations.
IBM Maximo Asset Monitor is a comprehensive solution that uses IoT sensors and AI to gain insights into the health and performance of physical assets.

## Slide 81: IoT Application Development
Section - 8

## Slide 82: Developing IoT Application
Hardware
Arduino UNO
Node MCU
IoT Development Framework
Arduino IDE
MQTT Server
Hive MQ
Raspberry Pi
Thonny

## Slide 83: Cloud Computing and IoT
Section - 9

## Slide 84: Introduction to Cloud Computing
Cloud computing : “Cloud computing is a model for enabling universal, convenient, on-demand network access to a shared pool of configurable computing resources (e.g., networks, servers, storage, applications, and services) that can be rapidly provisioned and released with minimal management effort or service provider interaction”.
Cloud computing is the delivery of computing services over the internet, by providing flexible, affordable, effective and efficient resources for development.
Application logic runs
on user’s computer
Application logic runs
in the cloud
Notes: 84

## Slide 85: Benefits of Cloud Computing
The availability of virtually unlimited storage and processing capabilities at low cost enabled the realization of a new computing model.
Large companies (like Amazon, Google, Facebook, etc.) widely adopted this paradigm for delivering services over the Internet, gaining both economical and technical benefits.
Cloud computing model is attractive since it frees the business owner from the need to invest in the infrastructure, renting resources according to needs and only paying for the usage.
Cloud Computing allows to decrease operating costs, that includes servers, storage, databases, networking, software, analytics, and intelligence.
Notes: 85

## Slide 86: Service Models of Cloud Computing
There are three main service models of cloud computing.
Infrastructure as a Service (IaaS)
Platform as a Service (PaaS)
Software as a Service (SaaS).
Each model represents a different part of the cloud computing stack.
Notes: 86

## Slide 87: Cloud Computing Services
Software as a Service (SaaS).
SaaS provides application-level services.
It is tailored to a wide variety of business needs.
Such as
  Customer relationship management (CRM)
  Marketing automation
  Business analytics.
Platform as a Service (PaaS).
Geared toward software development teams.
PaaS provides computing and storage infrastructure and also a development platform layer, with components such as
  Web servers
  Database management systems
  Software development kits (SDKs) for various programming languages.
Infrastructure as a Service (IaaS)
IaaS provides users access to raw computing resources.
Such as
  Processing power
  Data storage capacity
  Networking, in the context of a secure virtual data centre.

## Slide 88: Cloud Computing Services - Transportation analogy
Notes: 88

## Slide 89: Cloud Computing Services
Software
as a Service (SaaS)
Platform
as a Service (PaaS)
Infrastructure
as a Service (IaaS)
Traditional
On-Premises
Applications
Data
Runtime & Middleware
OS
Virtualization
Networking
Storage
Servers
Applications
Data
Runtime & Middleware
OS
Virtualization
Networking
Storage
Servers
Applications
Data
Runtime & Middleware
OS
Virtualization
Networking
Storage
Servers
Applications
Data
Runtime & Middleware
OS
Virtualization
Networking
Storage
Servers
You Manage
Vendor Manage
Notes: 89

## Slide 90: Software-as-a-Service (SaaS)
Complete software application as a service is provided to the user that is run and managed by the service provider.
It can also be called application as a service as a pay monthly, yearly etc. subscription.
In SaaS, user don't need to worry about software up-gradation and management.
A common example of a SaaS application is web-based email where you can send and receive email without having to manage the server that the email program is written.
Notes: 90

## Slide 91: Platform-as-a-Service (PaaS)
It provides a development environment to application developers.
Operating system, programming-language execution environment, database, web server, development tools, APIs, libraries, etc., will be provided by the cloud service provider.
Users have to build, manage and maintain the applications.
Application developers develop and run their software on a cloud platform instead of directly buying and managing the essential hardware and software layers.
AWS Lambda, Google App Engine, IBM Cloud Foundry, Oracle Cloud Platform, Red Hat-OpenShift, Zoho etc.
Notes: 91

## Slide 92: Infrastructure-as-a-Service (IaaS)
IaaS provides access to computing hardware, networking features, and data storage space.
Where the consumer is able to deploy and run software, which can include operating systems and applications.
The consumer does not manage or control the underlying cloud infrastructure but has control over operating systems, storage, and deployed applications.
This service provides the highest level access.
Notes: 92

## Slide 93: Cloud Computing Services Examples

## Slide 94: Types of Cloud Based on Services
Software-as-a-Service (SaaS):
  Complete software application as a service is provided to the user.
  It is application as a service as well, pay monthly, yearly etc. as subscription
Platform-as-a-Service (PaaS):
  Development tools, APIs, libraries etc. will be provided by the cloud service provider.
  Users have to build, manage and maintain the applications (provides platform to develop)
Infrastructure-as-a-Service (IaaS):
  Virtual Machines kind of support.
  Users shall manage the machines.
  Users shall select the OS and underlying applications.
  PAY as YOU use! (with IaaS approach, you choose virtual machines over physical machines)

## Slide 95: Fog Computing
Cisco coined the term fog computing (or fogging) in 2014, so it is new to the general public.
Fog and cloud computing are inter-twined.
In nature
  Fog is closer to Earth than clouds
In the tech world, it's the same;
  Fog is closer to end-users, bringing cloud capabilities to the ground.

## Slide 96: Fog Computing
Fog is an extension of cloud computing that consists of multiple edge nodes directly connected to physical devices.
The considerable processing power of edge nodes allows them to compute large amounts of data without sending them to distant servers.

## Slide 97: Data Flow – Smart Farm IoT System
Data Flow
Cloud Provider
Fog Devices
Microcontroller node
IoT Sensor
Farm

## Slide 98: Fog Computing vs. Cloud Computing
Fog Computing
Multiple Nodes and Nodes Connected to cloud
Cloud Computing
Directly the End-Devices are connected to Cloud

## Slide 99: How it Works?
An IoT system consists of sensors/devices which “talk” to the cloud through some kind of connectivity.
Once the data gets to the cloud, software processes it and then might decide to perform an action, such as sending an alert or automatically adjusting the sensors/devices without the need for the user.

## Slide 100: IoT Clouds

## Slide 101: IoT Application Development with IoT Cloud (Blynk)
Section - 10

## Slide 102: Developing IoT Application with IoT Cloud
Hardware
Arduino UNO
Node MCU
IoT Development Framework
Arduino IDE
IoT Cloud
Blynk
Arduino IoT Cloud
Raspberry Pi
Thonny

## Slide 103: IoT Cloud - Blynk
Blynk is a full suite of software, required to prototype, deploy, and remotely manage connected electronic devices at any scale: from personal IoT projects to millions of commercial connected products.
Blynk is a Cloud service with Paas type.
Fogwing
Google Cloud IoT Core

## Slide 104: Blynk Cloud
Blynk is considered a Platform as a Service (PaaS).
It provides a cloud-based platform for developers and businesses to build, deploy, and manage connected electronic devices.
Blynk provides the infrastructure to develop users' own IoT applications on top of Blynk's core functionalities rather than just providing a pre-built software service like a SaaS would.

## Slide 105: Blynk Cloud Service for IoT
Blynk is a comprehensive software suite that enables the prototyping, deployment, and remote management of connected electronic devices at any scale.
Blynk empowers users to connect their hardware to the cloud and create iOS, Android, and web applications, analyze real-time and historical data from devices, remotely control them from anywhere, receive important notifications, and much more.

## Slide 106: Components of the Blynk IoT Platform
Blynk.Console
Blynk.Apps
Blynk.Edgent &
Blynk Library
Edge + Agent = Edgent
Blynk.Cloud

## Slide 107: What You Need to Start Blynk
A Smart Phone with
Android OS v4.2 +
iOS v9+
Arduino like Board (For connecting with Cloud)
Blynk Board
ESP8266 Board (NodeMCU, WeMos D1, Witty Cloud )
IoT Hardware (For Sensor and Actuators)
Hardware Modules (any model) with Sensor and Actuators
ESP32
Nordic nRF51/nRF52
Arduino (any Model)
Raspberry Pi (any model)
Modules like:

## Slide 108: Include Header file/ Library for Blynk

## Slide 109: Blynk Authentication & initialization
We need to give the Proper Template Id and Authentication token for the Device identity and connectivity with Blynk Cloud :
To Start the communication with Blynk Cloud we have to call Blynk.begin method:
void setup()
{ // Debug console
Serial.begin(115200);
// Begins the Serial Communication with 115200 baudrate
Blynk.begin(auth, ssid, pass);
// Begins the communication with Blynk Cloud
}
void loop()
{
Blynk.run();
// Write Your Loop Code Here
}

## Slide 110: Read the value from Virtual Pin
BLYNK_WRITE()
This function used to read the changes or current value from dashboard.
Once the value is received from the Dashboard, we can process it for further changes on Hardware board.
BLYNK_WRITE() function is called every time the Virtual Pin 1 state changes.
BLYNK_WRITE() function reads the value of virtual variable from the Dashboard.
BLYNK_WRITE(V0)//V0 Virtual pin V0
{
// Set incoming value from pin V0 to a variable
int value = param.asInt();
}

## Slide 111: Write the Value on Virtual Pin
Blynk.virtualWrite(Vpin, value)
This function used to send the data to the Dashboard.
This function will send value or variable from Arduino board to Dashboard.
Syntax:
  Blynk.virtualWrite(Virtual pin, value)
Virtual Pin : Virtual Pin number assigned to particular widgets.
Value : variable or any static value
// You can send any value at any time.
Blynk.virtualWrite(V1, 10);
// Here we Write Value 10 to pin V1

## Slide 112: Demo Code : Blynk Cloud with NodeMCU -1
// Template ID, Device Name and Auth Token are provided by the Blynk.Cloud
// See the Device Info tab, or Template settings
#define BLYNK_TEMPLATE_ID "TMPLSU_PLFEC"
#define BLYNK_DEVICE_NAME "Quickstart Device"
#define BLYNK_AUTH_TOKEN "Zk6hlVfK1Ohi5Y8vWwy47gWnJCZf-c5d"
// Comment this out to disable prints and save space
#define BLYNK_PRINT Serial
#include <ESP8266WiFi.h> //Header File for the ESP8266 Wi-Fi Module support
#include <BlynkSimpleEsp8266.h> // Library file for the Blynk cloud support for //ESP8266
char auth[] = BLYNK_AUTH_TOKEN;
// Your WiFi credentials.
// Set password to "" for open networks.
char ssid[] = “IoT_Demo";
char pass[] = “diet@iot";
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
BlynkNodeMCU.demo

## Slide 113: Demo Code : Blynk Cloud with NodeMCU -2
// This function is called every time the Virtual Pin 0 state changes
BLYNK_WRITE(V0)
{
// Set incoming value from pin V0 to a variable
int value = param.asInt();
// Update state to the V1, virtual pin
Blynk.virtualWrite(V1, value);
}
// This function is called every time the device is connected to the Blynk.Cloud
BLYNK_CONNECTED()
{
//
}
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
BlynkNodeMCU.ino

## Slide 114: Demo Code : Blynk Cloud with NodeMCU -3
void setup()
{
// Debug console
Serial.begin(115200); // Begins the Serial Communication with 115200 baudrate
Blynk.begin(auth, ssid, pass); // Begins the communication with Blynk Cloud
}
void loop()
{
Blynk.run();
// You can inject your own code or combine it with other sketches.
// Check other examples on how to communicate with Blynk. Remember
// to avoid delay() function!
}
30
31
32
33
34
35
36
37
38
39
40
41
42
43
44
45
BlynkNodeMCU.ino

## Slide 115
bhushan.joshi@darshan.ac.in
+91 8485979997
Computer Engineering Department
Prof. Bhushan D. joshi
Internet of Things (IoT)
DU #2101CS631