## Slide 1: Unit-4 Pipelining and Computer Arithmetic
Vishal.kansagara@darshan.ac.in
8200601076
Computer Engineering Department
Prof. Vishal Kansagara
Computer System Architecture(CSA)
DU # 2101CS602

## Slide 2

Looping
Outline
  Flynn's taxonomy
  Parallel Processing
  Pipelining
  Arithmetic Pipeline
  Instruction Pipeline
  RISC Pipeline
  Addition and Subtraction
  Multiplication Algorithms (Booth Multiplication Algorithm)

## Slide 3: Flynn's taxonomy
Section - 1

## Slide 4: Flynn's taxonomy
Data Stream
Instruction Stream
SISD
SIMD
Single
Multiple
Single
Multiple
MISD
MIMD

## Slide 5: Single Instruction Single Data & Single Instruction Multiple Data
Single Instruction Single Data (SISD)
SISD represents the organization of a single computer containing a control unit, a processor unit, and a memory unit.
Instructions are executed sequentially and the system may or may not have internal parallel processing capabilities.
Single Instruction Multiple Data (SIMD)
SIMD represents an organization that includes many processing units under the supervision of a common control unit.
All processors receive the same instruction from the control unit but operate on different items of data.

## Slide 6: Multiple Instruction Single Data & Multiple Instruction Multiple Data
Multiple Instruction Single Data (MISD)
There is no computer at present that can be classified as MISD.
MISD structure is only of theoretical interest since no practical system has been constructed using this organization.
Multiple Instruction Multiple Data (MIMD)
MIMD organization refers to a computer system capable of processing several programs at the same time.
Most multiprocessor and multicomputer systems can be classified in this category.
Contains multiple processing units.
Execution of multiple instructions on multiple data.

## Slide 7: Parallel Processing
Section - 2

## Slide 8: Parallel Processing
Parallel processing is a term used to denote a large class of techniques that are used to provide simultaneous data-processing tasks for the purpose of increasing the computational speed of a computer system.
Purpose of parallel processing is to speed up the computer processing capability and increase its throughput.
Throughput:
The amount of processing that can be accomplished during a given interval of time.

## Slide 9: Pipelining
Section - 3

## Slide 10: Pipelining
Pipeline is a technique of decomposing a sequential process into sub operations, with each sub process being executed in a special dedicated segment that operates concurrently with all other segments.
A pipeline can be visualized as a collection of processing segments through which binary information flows.
Each segment performs partial processing dictated by the way the task is partitioned.
The result obtained from the computation in each segment is transferred to the next segment in the pipeline.
The registers provide isolation between each segment.
The technique is efficient for those applications that need to repeat the same task many times with different sets of data.

## Slide 11: Pipelining example
for
R1
R2
Multiplier
R3
R4
Adder
R5

## Slide 12: Pipelining
General structure of four segment pipeline
S1
R1
S2
R2
S3
R3
S4
R4
Clock
Input

## Slide 13: Space-time Diagram
1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 2 | 3 | 4 | 5 | 6 | 7
Clock cycles
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Segment
1
2
3
4
Segment
1
2
3
4
Non Pipelined Architecture
Pipelined Architecture

## Slide 14: Speedup
Speedup of a pipeline processing over an equivalent non-pipeline processing is defined by the ratio
If number of tasks in pipeline increases w.r.t. number of segments then becomes larger than , under this condition speedup becomes
Assuming time to process a task in pipeline and non-pipeline circuit is same then
Theoretically maximum speedup achieved is the number of segments in the pipeline.

## Slide 15: Arithmetic Pipeline
Section - 4

## Slide 16: Arithmetic Pipeline
Usually found in high speed computers.
Used to implement floating point operations, multiplication of fixed point numbers and similar operations.
Example:
Consider an example of floating point addition and subtraction.
A and B are two fractions that represent the mantissas and a and b are the exponents.

## Slide 17: Example of Arithmetic Pipeline
Consider the two normalized floating-point numbers:
X = 0.9504 x 103 Y = 0.8200 x 102
Segment-1: The larger exponent is chosen as the exponent of result.
Segment-2: Aligning the mantissa numbers
X = 0.9504 x 103 Y = 0.0820 x 103
Segment-3: Addition of the two mantissas produces the sum
Z = 1.0324 x 103
Segment-4: Normalize the result
Z = 0.10324 x 104
The sub-operations that are performed in the four segments are:
  Compare the exponents
  Align the mantissas
  Add or subtract the mantissas
  Normalize the result

## Slide 18
R
Compare exponents by subtraction
R
Choose exponent
R
Adjust exponent
R
Exponents
a
b
R
Align mantissas
R
Mantissas
A
B
Difference
Add or subtract mantissas
R
Normalize result
R
Segment 1:
Segment 2:
Segment 3:
Segment 4:

## Slide 19: Instruction Pipeline
Section - 5

## Slide 20: Instruction Pipeline
In the most general case, the computer needs to process each instruction with the following sequence of steps
  Fetch the instruction from memory.
  Decode the instruction.
  Calculate the effective address.
  Fetch the operands from memory.
  Execute the instruction.
  Store the result in the proper place.
Different segments may take different times to operate on the incoming information.
Some segments are skipped for certain operations.
The design of an instruction pipeline will be most efficient if the instruction cycle is divided into segments of equal duration.

## Slide 21: Instruction Pipeline
Assume that the decoding of the instruction can be combined with the calculation of the effective address into one segment.
Assume further that most of the instructions place the result into a processor registers so that the instruction execution and storing of the result can be combined into one segment.
This reduces the instruction pipeline into four segments.
  FI: Fetch an instruction from memory
  DA: Decode the instruction and calculate the effective address of the operand
  FO: Fetch the operand
  EX: Execute the operation

## Slide 22: Four segment CPU pipeline
Fetch instruction from memory
Decode instruction & calculate effective address
Branch?
Fetch operand from memory
Execute instruction
Interrupt?
Interrupt handling
Update PC
Empty pipe
Segment1:
Segment2:
Segment3:
Segment4:
yes
yes
no
no

## Slide 23: Space-time Diagram
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
FI | DA | FO | EX |  |  |  |  |  |  |  |  | 
 | FI | DA | FO | EX |  |  |  |  |  |  |  | 
 |  | FI | DA | FO | EX |  |  |  |  |  |  | 
 |  |  | FI | DA | FO | EX |  |  |  |  |  | 
 |  |  |  | FI | DA | FO | EX |  |  |  |  | 
 |  |  |  |  | FI | DA | FO | EX |  |  |  | 
 |  |  |  |  |  | FI | DA | FO | EX |  |  | 
Step:
Instruction 1
2
3
4
5
6
7

## Slide 24: Space-time Diagram
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
FI | DA | FO | EX |  |  |  |  |  |  |  |  | 
 | FI | DA | FO | EX |  |  |  |  |  |  |  | 
 |  | FI | DA | FO | EX |  |  |  |  |  |  | 
 |  |  | FI | - | - | FI | DA | FO | EX |  |  | 
 |  |  |  | - | - | - | FI | DA | FO | EX |  | 
 |  |  |  |  |  |  |  | FI | DA | FO | EX | 
 |  |  |  |  |  |  |  |  | FI | DA | FO | EX
2
3
4
5
6
7
(Branch)
Step:
Instruction 1

## Slide 25: Pipeline Conflict & Data Dependency
Pipeline Conflict
There are three major difficulties that cause the instruction pipeline conflicts.
  Resource conflicts caused by access to memory by two segments at the same time. Most of these conflicts can be resolved by using separate instruction and data memories.
  Data dependency conflicts arise when an instruction depends on the result of a previous instruction, but this result is not yet available.
  Branch difficulties arise from branch and other instructions that change the value of PC.
Data Dependency
Data dependency occurs when an instruction needs data that are not yet available.
Pipelined computers deal with such conflicts between data dependencies in a variety of ways as follows:
  Hardware Interlocks
  Operand forwarding
  Delayed load

## Slide 26: Handling Branch Instructions
The branch instruction breaks the normal sequence of the instruction stream, causing difficulties in the operation of the instruction pipeline.
Hardware techniques available to minimize the performance degradation caused by instruction branching are as follows:
  Pre-fetch target
  Branch target buffer
  Loop buffer
  Branch prediction
  Delayed branch

## Slide 27: RISC Pipeline
Section - 6

## Slide 28: RISC Pipeline (Three segment instruction pipeline)
Because of the fixed-length instruction format, the decoding of the operation can occur at the same time as the register selection.
Since all the operands are in registers, there is no need for calculating an effective address or fetching of operands from memory.
RISC has main two facilities:
  Single-cycle instruction execution
  Compiler support
Mainly three types of instructions in RISC:
  Data manipulation instructions
  Data transfer instructions
  Program control instructions
The instruction cycle can be divided into three sub-operations and implemented in three segments:
  I : Instruction fetch
  A : ALU operation
  E : Execute instruction

## Slide 29: Delayed Load
1 | 2 | 3 | 4 | 5 | 6
I | A | E |  |  | 
 | I | A | E |  | 
 |  | I | A | E | 
 |  |  | I | A | E
Clock cycles:
Load R1
Load R2
Add R1+R2
Store R3
Pipeline timing with data conflict
1 | 2 | 3 | 4 | 5 | 6 | 7
I | A | E |  |  |  | 
 | I | A | E |  |  | 
 |  | I | A | E |  | 
 |  |  | I | A | E | 
 |  |  |  | I | A | E
Clock cycles:
Load R1
Load R2
Add R1+R2
Store R3
No-operation
Pipeline timing with delayed load

## Slide 30: Delayed Branch
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
I | A | E |  |  |  |  |  |  | 
 | I | A | E |  |  |  |  |  | 
 |  | I | A | E |  |  |  |  | 
 |  |  | I | A | E |  |  |  | 
 |  |  |  | I | A | E |  |  | 
 |  |  |  |  | I | A | E |  | 
 |  |  |  |  |  | I | A | E | 
 |  |  |  |  |  |  | I | A | E
Clock cycle:
Load R1
Increment R2
Add R3+R4
Subtract R6-R5
Branch to X
No operation
No operation
Instruction in X
Using no-operation instructions

## Slide 31: Delayed Branch
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
I | A | E |  |  |  |  | 
 | I | A | E |  |  |  | 
 |  | I | A | E |  |  | 
 |  |  | I | A | E |  | 
 |  |  |  | I | A | E | 
 |  |  |  |  | I | A | E
Clock cycle:
Load R1
Increment R2
Add R3+R4
Subtract R6-R5
Branch to X
Instruction in X
Rearranging the instructions

## Slide 32: Addition and Subtraction
Section - 1

## Slide 33: Addition and Subtraction
Operation | Add Magnitudes | Subtract Magnitudes |  | 
 |  | When A > B | When A < B | When A = B
(+A) + (+B) | + (A + B) |  |  | 
(+A) + (-B) |  | + (A - B) | - (B - A) | + (A - B)
(-A) + (+B) |  | - (A - B) | + (B - A) | + (A - B)
(-A) + (-B) | - (A + B) |  |  | 
(+A) - (+B) |  | + (A - B) | - (B - A) | + (A - B)
(+A) - (-B) | + (A + B) |  |  | 
(-A) - (+B) | - (A + B) |  |  | 
(-A) - (-B) |  | - (A - B) | + (B - A) | + (A - B)

## Slide 34: Flowchart for Addition & Subtraction
Subtract operation
Add operation
Minuend in A
Subtrahend in B
Augend in A
Addend in B
As⊕Bs
As⊕Bs
EA ← A+B’+1
AVF ← 0
EA ← A+B
E
AVF ← E
A ← A’
A
A ← A+1
As ← As’
As ← 0
END
(result is in A and As)
= 0
= 1
= 1
= 0
As = Bs
As = Bs
As ≠ Bs
As ≠ Bs
= 0
= 1
A < B
A ≥ B
≠ 0
= 0
As = Sign bit of A
Bs = Sign bit of B
AVF = add overflow flip-flop
E = Carry

## Slide 35: Multiplication Algorithms (Booth Multiplication Algorithm)
Section - 2

## Slide 36: Multiplication
Traditional way of binary multiplication
23
19
10111
10011
x
x
10111
10111
00000
00000
10111
110110101
437
Multiply operation
= 1
= 0
SC
= 0
≠ 0
Multiplicand in B Multiplier in Q
END
(PRODUCT is in AQ)

## Slide 37: Perform 23 x 19
Multiplicand B = 10111 | E | A | Q | SC
Multiplier in Q | 0 | 00000 | 10011 | 101
Qn = 1; add B |  | 10111 |  | 
First partial product | 0 | 10111 |  | 
Shift right EAQ | 0 | 01011 | 11001 | 100
Qn = 1; add B |  | 10111 |  | 
Second partial product | 1 | 00010 |  | 
Shift right EAQ | 0 | 10001 | 01100 | 011
Qn = 0; shift right EAQ | 0 | 01000 | 10110 | 010
Qn = 0; shift right EAQ | 0 | 00100 | 01011 | 001
Qn = 1; add B |  | 10111 |  | 
Fifth partial product | 0 | 11011 |  | 
Shift right EAQ | 0 | 01101 | 10101 | 000
Final product in AQ = 0110110101 |  |  |  | 

## Slide 38: Multiply (-9) x (-13) using Booth Algorithm
 |  | = 10111 = 01001 |  |  |  | 
 |  | Initial | 00000 | 10011 | 0 | 101
1 | 0 | Subtract BR | 01001 |  |  | 
 |  |  | 01001 |  |  | 
 |  | ashr | 00100 | 11001 | 1 | 100
1 | 1 | ashr | 00010 | 01100 | 1 | 011
0 | 1 | Add BR | 10111 |  |  | 
 |  |  | 11001 |  |  | 
 |  | ashr | 11100 | 10110 | 0 | 010
0 | 0 | ashr | 11110 | 01011 | 0 | 001
1 | 0 | Subtract BR | 01001 |  |  | 
 |  |  | 00111 |  |  | 
 |  | ashr | 00011 | 10101 | 1 | 000
 |  | Initial | 00000 | 10011 | 0 | 101
1 | 0 | Subtract BR | 01001 |  |  | 
 |  |  | 01001 |  |  | 
 |  | ashr | 00100 | 11001 | 1 | 100
1 | 1 | ashr | 00010 | 01100 | 1 | 011
0 | 1 | Add BR | 10111 |  |  | 
 |  |  | 11001 |  |  | 
 |  | ashr | 11100 | 10110 | 0 | 010
0 | 0 | ashr | 11110 | 01011 | 0 | 001
1 | 0 | Subtract BR | 01001 |  |  | 
 |  |  | 00111 |  |  | 
 |  | ashr | 00011 | 10101 | 1 | 000

## Slide 39: Booth Multiplication Algorithm
Multiply operation
= 01
= 10
SC
= 0
≠ 0
Multiplicand in BR Multiplier in QR
END
= 00
= 11

## Slide 40: Thank you
