## Slide 1: Unit-5 Input-Output Organization
Vishal.kansagara@darshan.ac.in
8200601076
Computer Engineering Department
Prof. Vishal Kansagara
Computer System Architecture(CSA)
DU # 2101CS602

## Slide 2

Looping
Outline
  Input-output interface
  Asynchronous Data Transfer
  Modes Of Transfer
  Priority Interrupt
  DMA
  Input-Output Processor (IOP)

## Slide 3: Input-output interface
Section - 1

## Slide 4: Peripherals, I/O Bus and Interface

## Slide 5: Peripherals, I/O Bus and Interface
Peripherals: Input-output device attached to the computer are called peripherals.
The I/O bus consists of data lines, address lines, and control lines.
The magnetic disk, printer, display terminal and keyboard are employed in practically any general purpose computer.
Each peripheral device has associated with it an interface unit.
Each interface decodes the address and control received from the I/O bus, interprets them for the peripheral, and provides signals for the peripheral controller.
It also synchronizes the data flow and supervises the transfer between peripheral and processor.
Each peripheral has its own controller that operates the particular electromechanical device.
For example, the printer controller controls the paper motion, the print timing, and the selection of printing characters.

## Slide 6: Peripherals, I/O Bus and Interface
The I/O bus from the processor is attached to all peripheral interfaces.
To communicate with a particular device, the processor places a device address on the address lines.
Each interface attached to the I/O bus contains an address decoder that monitors the address lines.
When the interface detects its own address, it activates the path between the bus lines and the device that it controls.
All peripherals whose address does not correspond to the address in the bus are disabled by their interface, and selected responds to the function code and proceeds to execute it.
The function code is referred to as an I/O command.
There are four types of commands that an interface may receive. They are classified as control, status, data output, and data input.

## Slide 7: Peripherals, I/O Bus and Interface
A control command is issued to activate the peripheral and to inform it what to do.
For example, a magnetic tape unit may be instructed to backspace the tape by one record, to rewind the tape, or to start the tape moving in the forward direction.
A status command is used to test various status conditions in the interface and the peripheral.
For example, the computer may wish to check the status of the peripheral before a transfer is initiated.
During the transfer, one or more errors may occur which are detected by the interface.
These errors are designated by setting bits in a status register that the processor can read at certain intervals.
A data output command causes the interface to respond by transferring data from the bus into one of its registers.
The computer starts the tape moving by issuing a control command.

## Slide 8: Peripherals, I/O Bus and Interface
The processor then monitors the status of the tape by means of a status command.
When the tape is in the correct position, the processor issues a data output command.
The interface responds to the address and command and transfers the information from the data lines in the bus to its buffer register.
The interface that communicates with the tape controller and sends the data to be stored on tape.
The data input command is the opposite of the data output.
In this case the interface receives an item of data from the peripheral and places it in its buffer register.
The processor checks if data are available by means of a status command and then issues a data input command.
The interface places the data on the data lines, where they are accepted by the processor.

## Slide 9: I/O interface
CS | RS1 | RS0 | Register Selected
0 | X | X | None: data bus in high impedance
1 | 0 | 0 | Port A register
1 | 0 | 1 | Port B register
1 | 1 | 0 | Control register
1 | 1 | 1 | Status register

## Slide 10: I/O Interface
It consists of two data registers called ports, a control register, a status register, bus buffers, and timing and control circuit.
The interface communicates with the CPU through the data bus.
The chip select and register select inputs determine the address assigned to the interface.
The I/O read and writes are two control lines that specify an input or output, respectively.
The four registers communicate directly with the I/O device attached to the interface.
The I/O data to and from the device can be transferred into either port A or port B.
If the interface is connected to a printer, it will only output data, and if it services a character reader, it will only input data.
A magnetic disk unit transfers data in both directions but not at the same time, so the interface can use bidirectional lines.
A command is passed to the I/O device by sending a word to the appropriate interface register.

## Slide 11: I/O Interface
The control register receives control information from the CPU. By loading appropriate bits into the control register, the interface and the I/O device attached to it can be placed in a variety of operating modes.
For example, port A may be defined as an input port and port B as an output port.
A magnetic tape unit may be instructed to rewind the tape or to start the tape moving in the forward direction.
The bits in the status register are used for status conditions and for recording errors that may occur during the data transfer.
For example, a status bit may indicate that port A has received a new data item from the I/O device.
Another bit in the status register may indicate that a parity error has occurred during the transfer.
The interface registers communicate with the CPU through the bidirectional data bus.

## Slide 12: I/O Interface
The address bus selects the interface unit through the chip select and the two register select inputs.
A circuit must be provided externally (usually, a decoder) to detect the address assigned to the interface registers.
This circuit enables the chip select (CS) input when the interface is selected by the address bus.
The two register select inputs RS1 and RS0 are usually connected to the two least significant lines of the address bus.
These two inputs select one of the four registers in the interface as specified in the table accompanying the diagram.
The content of the selected register is transfer into the CPU via the data bus when the I/O read signal is enables.
The CPU transfers binary information into the selected register via the data bus when the I/O write input is enabled.

## Slide 13: Asynchronous Data Transfer
Section - 1

## Slide 14: Asynchronous Data Transfer
Asynchronous data transfer between two independent units requires that control signals be transmitted between the communicating units to indicate the time at which data is being transmitted.
Two ways of achieving
  Strobe
  Handshaking

## Slide 15: Strobe Method
1.1 Source initiated Strobe
Source unit
Destination unit
Data Bus
Strobe
Valid Data
Data
Strobe
1.2 Destination initiated Strobe
Source unit
Destination unit
Data Bus
Strobe
Valid Data
Data
Strobe

## Slide 16: 2.1 Source initiated Handshake
Source unit
Destination unit
Data bus
Data valid
Valid Data
Data bus
Data accepted
Data accepted
Data valid
Place data on bus.
Enable data valid.
Accept data from bus.
Enable data accepted.
Disable data valid.
Invalidate data on bus.
Disable data accepted.
Ready to accept data (initial state).
Source unit
Destination unit

## Slide 17: 2.2 Destination initiated Handshake
Source unit
Destination unit
Data bus
Data valid
Ready for data
Ready for data
Data valid
Data bus
Valid Data
Place data on bus.
Enable data valid.
Ready to accept data.
Enable Ready for data.
Source unit
Destination unit
Accept data from bus.
Disable Ready for data.
Disable data valid.
Invalid data on bus
(initial state).

## Slide 18: Asynchronous Serial Transfer
Rules for transmission
  When a character is not being sent, the line is kept in the 1-state.
  The initiation of a character transmission is detected from the start bit, which is always 0.
  The character bits always follow the start bit.
  After the last bit of the character is transmitted, a stop bit is detected when the line returns to the 1-state for at least one bit time.
Start
bit
Stop
bits
Character bit
1
1
0
0
0
1
0
1

## Slide 19: Modes Of Transfer
Section - 2

## Slide 20: Modes of Transfer
Data transfer between the central computer and I/O devices may be handled in a variety of modes.
Some modes use the CPU as an intermediate path; others transfer the data directly to and from the memory unit.
Data transfer to and from peripherals may be handled in one of three possible modes:
  Programmed I/O
  Interrupt-initiated I/O
  Direct memory access (DMA)

## Slide 21: Programmed I/O
CPU
Interface
Data register
Status register
F
I/O
device
Data bus
I/O bus
Data valid
Data accepted
Address bus
I/O read
I/O write
Read Status register
Check flag bit
Read Data register
Transfer data to memory
Continue with program
Flag
Operation complete?
= 0
= 1
yes
no

## Slide 22: Interrupt-initiated I/O
An alternative to the CPU constantly monitoring the flag is to let the interface inform the computer when it is ready to transfer data.
While the CPU is running a program, it does not check the flag.
However, when the flag is set, the computer is momentarily interrupted from proceeding with current program and is informed of the fact that the flag has been set.
The CPU deviates from what it is doing to take care of the input or output transfer.
After the transfer is completed, the computer returns to the previous program to continue what it was doing before the interrupt.

## Slide 23: Priority Interrupt
Section - 3

## Slide 24: Priority Interrupt (Daisy-Chaining Technique)
Determines which interrupt is to be served first when two or more requests are made simultaneously
Also determines which interrupts are permitted to interrupt the computer while another is being serviced.
Higher priority interrupts can make requests while servicing a lower priority interrupt.
Device 1
PI
PO
Device 2
PI
PO
Device 3
PI
PO
CPU
INT
INTACK
VAD 1
VAD 2
VAD 3
Processor data bus
Interrupt request
Interrupt acknowledge
To next
device

## Slide 25: DMA (Direct Memory Access)
Section - 4

## Slide 26: DMA (Direct Memory Access)
The transfer of data between a fast storage device such as magnetic disk and memory is often limited by the speed of the CPU.
Removing the CPU from the path and letting the peripheral device manage the memory buses directly would improve the speed of transfer.
This transfer technique is called direct memory access (DMA).
During DMA, CPU is idle and has no control of the memory buses.
A DMA controller takes over the buses to manage the transfer directly between the I/O device and memory.
BR
BG
ABUS
DBUS
RD
WR
CPU
Bus request
Bus granted
Address bus
Data bus
Read
Write
High-impedance (disabled) when BG is enabled

## Slide 27: DMA Controller
DMA Controller
DMA controller - Interface which allows I/O transfer directly between Memory and Device, freeing CPU for other tasks
CPU initializes DMA Controller by sending memory address and the block size (number of words).
BR
BG
DS
RS
RD
WR
Control logic
Bus request
Bus grant
Read
Write
Interrupt
Register select
DMA Select
Interrupt
Data bus buffers
Data bus
Internal Bus
Address bus buffers
Address register
Word count register
Control register
Address bus
DMA Acknowledge
DMA Request
to I/O device

## Slide 28: Input-Output Processor (IOP)
Section - 5

## Slide 29: Input-Output Processor (IOP)
Memory Unit
Central Processing Unit (CPU)
Input-Output Processor
PD
PD
PD
PD
Peripheral Device
Memory Bus
I/O Bus

## Slide 30
Send instruction to test IOP path
Transfer status word to memory location
If status OK, send start I/O instruction to IOP
Access memory for IOP program
CPU continues with another program
Conduct I/O transfers using DMA; prepare status report
I/O transfer completed; interrupt CPU
Request IOP status
Transfer status word to memory location
Check status word for correct transfer
CPU operations
IOP operations
Continue
CPU – IOP Communication

## Slide 31: Thank you
